## Slide 1: Network+ Guide to Networks 6th Edition
Chapter 3
Transmission Basics and Networking Media

## Slide 2: Objectives
Explain basic data transmission concepts, including full duplexing, attenuation, latency, and noise
Describe the physical characteristics of coaxial cable, STP, UTP, and fiber-optic media
Compare the benefits and limitations of different networking media
Explain the principles behind and uses for serial cables
Identify wiring standards and the best practices for cabling buildings and work areas

## Slide 3: Transmission Basics
Transmit
  Issue signals along network medium
Transmission
  Process of transmitting
  Signal progress after transmitting
Transceiver
  Transmits and receives signals

## Slide 4: Analog and Digital Signaling
Important data transmission characteristic
  Signaling type: analog or digital
Volt
  Electrical current pressure
Electrical signal strength
  Directly proportional to voltage
  Signal voltage
Signals
  Current, light pulses, electromagnetic waves

## Slide 5: Analog and Digital Signaling (cont’d.)
Analog data signals
  Voltage varies continuously
Fundamental properties of analog signals
  Amplitude
    Measure of strength at given point in time
  Frequency
    Number of times amplitude cycles over fixed time
  Wavelength
    Distance between one peak and the next
  Phase
    Progress of wave over time compared to a fixed point

## Slide 6
Figure 3-1 An example of an analog signal
Courtesy Course Technology/Cengage Learning

## Slide 7
Figure 3-2 Waves with a 90 degree phase difference
Courtesy Course Technology/Cengage Learning

## Slide 8: Analog and Digital Signaling (cont’d.)
Analog signal benefit over digital
  More variable
    Convey greater subtleties with less energy
Drawback of analog signals
  Varied and imprecise voltage
    Susceptible to transmission flaws
Digital signals
  Pulses of voltages
    Positive voltage represents a 1
    Zero voltage represents a 0

## Slide 9
Figure 3-3 An example of a digital signal
Courtesy Course Technology/Cengage Learning
Figure 3-4 Components of a byte
Courtesy Course Technology/Cengage Learning

## Slide 10: Analog and Digital Signaling (cont’d.)
Convert byte to decimal number
  Determine value represented by each bit
  Add values
Convert decimal number to a byte
  Reverse the process
Convert between binary and decimal
  By hand or calculator

## Slide 11: Analog and Digital Signaling (cont’d.)
Digital signal benefit over analog signal
  More reliable
  Less severe noise interference
Digital signal drawback
  Many pulses required to transmit same information
Overhead
  Nondata information
  Required for proper signal routing and interpretation
  Example: network layer addressing information

## Slide 12: Data Modulation
Data relies on digital transmission
Network connection may handle only analog signals
Modem
  Accomplishes translation
  Modulator/demodulator
Data modulation
  Technology modifying analog signals
  Make data suitable for carrying over communication path

## Slide 13: Data Modulation (cont’d.)
Carrier wave
  Combined with another analog signal
  Produces unique signal
    Transmitted from one node to another
  Preset properties
  Purpose: convey information
Information wave (data wave)
  Added to carrier wave
  Modifies one carrier wave property

## Slide 14: Data Modulation (cont’d.)
Frequency modulation
  Carrier frequency modified by application of data signal
Amplitude modulation
  Carrier signal amplitude modified by application of data signal
Digital subscriber line (DSL)
  Also makes use of modulation

## Slide 15
Figure 3-5 A carrier wave modified through frequency modulation
Courtesy Course Technology/Cengage Learning

## Slide 16: Simplex, Half-Duplex, and Duplex
Simplex
  Signals travel in one direction
Half-duplex transmission
  Signals travel in both directions
    One at a time
  Shared communication channel
Full-duplex
  Signals travel in both directions simultaneously
  Used on data networks

## Slide 17
Figure 3-6 Simplex, half-duplex, and full-duplex transmission
Courtesy Course Technology/Cengage Learning

## Slide 18: Simplex, Half-Duplex, and Duplex (cont’d.)
Channel
  Distinct communication path between nodes
  Separated physically or logically
Full duplex advantage
  Increases speed of data travel
Some modems and NICs allow specifying half- or full-duplex communication
  Modern NICs use full duplex by default

## Slide 19: Multiplexing
Multiplexing
  Multiple signals
  Travel simultaneously over one medium
Subchannels
  Logical multiple smaller channels
Multiplexer (mux)
  Combines many channel signals
Demultiplexer (demux)
  Separates combined signals
  Regenerates them

## Slide 20: Multiplexing (cont’d.)
Time division multiplexing (TDM)
  Divides channel into multiple time intervals
Courtesy Course Technology/Cengage Learning
Figure 3-7 Time division multiplexing

## Slide 21: Multiplexing (cont’d.)
Statistical multiplexing
  Transmitter assigns slots to nodes
    According to priority, need
  More efficient than TDM
Courtesy Course Technology/Cengage Learning
Figure 3-8 Statistical multiplexing

## Slide 22: Multiplexing (cont’d.)
Frequency division multiplexing (FDM)
  Unique frequency band for each communications subchannel
  Cellular telephone transmission
  DSL Internet access
Courtesy Course Technology/Cengage Learning
Figure 3-9 Frequency division multiplexing

## Slide 23: Multiplexing (cont’d.)
Wavelength division multiplexing (WDM)
  One fiber-optic connection
  Carries multiple light signals simultaneously
Courtesy Course Technology/Cengage Learning
Figure 3-10 Wavelength division multiplexing

## Slide 24: Multiplexing (cont’d.)
Dense wavelength division multiplexing (DWDM)
  Used on most modern fiber-optic networks
  Extraordinary capacity

## Slide 25: Relationships Between Nodes
Point-to-point transmission
  One transmitter and one receiver
Point-to-multipoint transmission
  One transmitter and multiple receivers
Broadcast transmission
  One transmitter and multiple, undefined receivers
  Used on wired and wireless networks
  Simple and quick
Nonbroadcast
  One transmitter and multiple, defined recipients

## Slide 26
Courtesy Course Technology/Cengage Learning
Figure 3-11 Point-to-point versus broadcast transmission

## Slide 27: Throughput and Bandwidth
Throughput
  Amount of data transmitted during given time period
  Also called capacity or bandwidth
  Expressed as bits transmitted per second
Bandwidth (strict definition)
  Difference between highest and lowest frequencies medium can transmit
  Range of frequencies
  Measured in hertz (Hz)

## Slide 28
Courtesy Course Technology/Cengage Learning
Table 3-1 Throughput measures

## Slide 29: Baseband and Broadband
Baseband transmission
  Digital signals sent through direct current (DC) pulses applied to wire
  Requires exclusive use of wire’s capacity
  Transmit one signal (channel) at a time
  Example: Ethernet
Broadband transmission
  Signals modulated as radio frequency (RF) analog waves
  Uses different frequency ranges
  Does not encode information as digital pulses

## Slide 30: Transmission Flaws
Noise
  Any undesirable influence degrading or distorting signal
Types of noise
  EMI (electromagnetic interference)
    Example: radio frequency interference
  Cross talk
    Signal on one wire infringes on adjacent wire signal
    Near end cross talk (NEXT) occurs near source

## Slide 31
Courtesy Course Technology/Cengage Learning
Figure 3-12 Cross talk between wires in a cable

## Slide 32: Transmission Flaws (cont’d.)
Attenuation
  Loss of signal’s strength as it travels away from source
Signal boosting technology
  Analog signals pass through amplifier
    Noise also amplified
  Regeneration
    Digital signals retransmitted in original form
    Repeater: device regenerating digital signals
  Amplifiers and repeaters
    OSI model Physical layer

## Slide 33
Courtesy Course Technology/Cengage Learning
Figure 3-14 A digital signal distorted by noise and then repeated
Figure 3-13 An analog signal distorted by noise and then amplified
Courtesy Course Technology/Cengage Learning

## Slide 34: Transmission Flaws (cont’d.)
Latency
  Delay between signal transmission and receipt
  May cause network transmission errors
Latency causes
  Cable length
  Intervening connectivity device
Round trip time (RTT)
  Time for packet to go from sender to receiver, then back from receiver to sender

## Slide 35: Common Media Characteristics
Selecting transmission media
  Match networking needs with media characteristics
Physical media characteristics
  Throughput
  Cost
  Noise immunity
  Size and scalability
  Connectors and media converters

## Slide 36: Throughput
Most significant factor in choosing transmission method
Causes of throughput limitations
  Laws of physics
  Signaling and multiplexing techniques
  Noise
  Devices connected to transmission medium
Fiber-optic cables allow faster throughput
  Compared to copper or wireless connections

## Slide 37: Cost
Precise costs difficult to pinpoint
Media cost dependencies
  Existing hardware, network size, labor costs
Variables influencing final cost
  Installation cost
  New infrastructure cost versus reuse
  Maintenance and support costs
  Cost of lower transmission rate affecting productivity
  Cost of downtime
  Cost of obsolescence

## Slide 38: Noise Immunity
Noise distorts data signals
  Distortion rate dependent upon transmission media
Fiber-optic: least susceptible to noise
Limit noise impact on network
  Cable installation
    Far away from powerful electromagnetic forces
  Select media protecting signal from noise
  Antinoise algorithms

## Slide 39: Size and Scalability
Three specifications
  Maximum nodes per segment
  Maximum segment length
  Maximum network length
Maximum nodes per segment dependency
  Attenuation and latency
Maximum segment length dependency
  Attenuation and latency plus segment type

## Slide 40: Size and Scalability (cont’d.)
Segment types
  Populated: contains end nodes
  Unpopulated: no end nodes
    Also called link segment
Segment length limitation
  After certain distance, signal loses strength
    Cannot be accurately interpreted

## Slide 41: Connectors and Media Converters
Connectors
  Hardware connecting wire to network device
  Specific to particular media type
  Affect costs
    Installing and maintaining network
    Ease of adding new segments or nodes
    Technical expertise required to maintain network
Media converter
  Hardware enabling networks or segments running on different media to interconnect and exchange signals

## Slide 42
Courtesy of Omnitron Systems Technology
Figure 3-15 Copper wire-to-fiber media converter

## Slide 43: Coaxial Cable
Central metal core (often copper) surrounded by:
  Insulator
  Braided metal shielding (braiding or shield)
  Outer cover (sheath or jacket)
Figure 3-16 Coaxial cable
Courtesy Course Technology/Cengage Learning

## Slide 44: Coaxial Cable (cont’d.)
High noise resistance
Advantage over twisted pair cabling
  Carry signals farther before amplifier required
Disadvantage over twisted pair cabling
  More expensive
Hundreds of specifications
  RG specification number
  Differences: shielding and conducting cores
    Transmission characteristics

## Slide 45: Coaxial Cable (cont’d.)
Conducting core
  American Wire Gauge (AWG) size
  Larger AWG size, smaller wire diameter
Data networks usage
  RG-6
  RG-8
  RG-58
  RG-59

## Slide 46
Courtesy of MCM Electronics, Inc.
Figure 3-17 F-Type connector
© Igor Smichkov/Shutterstock.com
Figure 3-18 BNC connector

## Slide 47: Twisted Pair Cable
Color-coded insulated copper wire pairs
  0.4 to 0.8 mm diameter
  Encased in a plastic sheath
Courtesy Course Technology/Cengage Learning
Figure 3-19 Twisted pair cable

## Slide 48: Twisted Pair Cable (cont’d.)
More wire pair twists per foot
  More resistance to cross talk
  Higher-quality
  More expensive
Twist ratio
  Twists per meter or foot
High twist ratio
  Greater attenuation

## Slide 49: Twisted Pair Cable (cont’d.)
Hundreds of different designs
  Twist ratio, number of wire pairs, copper grade, shielding type, shielding materials
  1 to 4200 wire pairs possible
Wiring standard specification
  TIA/EIA 568
Most common twisted pair types
  Category (cat) 3, 5, 5e, 6, 6a, 7
  CAT 5 or higher used in modern LANs

## Slide 50: Twisted Pair Cable (cont’d.)
Advantages
  Relatively inexpensive
  Flexible
  Easy installation
  Spans significant distance before requiring repeater
  Accommodates several different topologies
Two categories
  Shielded twisted pair (STP)
  Unshielded twisted pair (UTP)

## Slide 51: STP (Shielded Twisted Pair)
Individually insulated
Surrounded by metallic substance shielding (foil)
  Barrier to external electromagnetic forces
  Contains electrical energy of signals inside
  May be grounded
Figure 3-20 STP cable
Courtesy Course Technology/Cengage Learning

## Slide 52: UTP (Unshielded Twisted Pair)
One or more insulated wire pairs
  Encased in plastic sheath
  No additional shielding
    Less expensive, less noise resistance
Courtesy Course Technology/Cengage Learning
Figure 3-21 UTP cable

## Slide 53: Comparing STP and UTP
Throughput
  STP and UTP can transmit the same rates
Cost
  STP and UTP vary
Connector
  STP and UTP use Registered Jack 45
  Telephone connections use Registered Jack 11

## Slide 54: Comparing STP and UTP (cont’d.)
Noise immunity
  STP more noise resistant
Size and scalability
  Maximum segment length for both: 100 meters

## Slide 55: Terminating Twisted Pair Cable
Patch cable
  Relatively short cable
  Connectors at both ends
Proper cable termination techniques
  Basic requirement for two nodes to communicate
Poor terminations:
  Lead to loss or noise
TIA/EIA standards
  TIA/EIA 568A
  TIA/EIA 568B

## Slide 56
Courtesy Course Technology/Cengage Learning
Figure 3-24 TIA/EIA 568A standard terminations
Courtesy Course Technology/Cengage Learning
Figure 3-25 TIA/EIA 568B standard terminations

## Slide 57: Terminating Twisted Pair Cable (cont’d.)
Straight-through cable
  Terminate RJ-45 plugs at both ends identically
Crossover cable
  Transmit and receive wires on one end reversed
Figure 3-26 RJ-45 terminations on a crossover cable
Courtesy Course Technology/Cengage Learning

## Slide 58: Terminating Twisted Pair Cable (cont’d.)
Termination tools
  Wire cutter
  Wire stripper
  Crimping tool
After making cables:
  Verify data transmit and receive

## Slide 59: Fiber-Optic Cable
Fiber-optic cable (fiber)
  One or more glass or plastic fibers at its center (core)
Data transmission
  Pulsing light sent from laser or light-emitting diode (LED) through central fibers
Cladding
  Layer of glass or plastic surrounding fibers
  Different density from glass or plastic in strands
  Reflects light back to core
  Allows fiber to bend

## Slide 60: Fiber-Optic Cable (cont’d.)
Plastic buffer outside cladding
  Protects cladding and core
  Opaque to absorb escaping light
  Surrounded by Kevlar (polymeric fiber) strands
Plastic sheath covers Kevlar strands
Figure 3-30 A fiber-optic cable
Courtesy of Optical Cable Corporation

## Slide 61: Fiber-Optic Cable (cont’d.)
Different varieties
  Based on intended use and manufacturer
Figure 3-31 Zipcord fiber-optic patch cable
Courtesy Course Technology/Cengage Learning

## Slide 62: Fiber-Optic Cable (cont’d.)
Benefits over copper cabling
  Extremely high throughput
  Very high noise resistance
  Excellent security
  Able to carry signals for longer distances
  Industry standard for high-speed networking
Drawbacks
  More expensive than twisted pair cable
  Requires special equipment to splice

## Slide 63: SMF (Single-Mode Fiber)
Consists of narrow core (8-10 microns in diameter)
  Laser-generated light travels over one path
    Little reflection
  Light does not disperse as signal travels
Can carry signals many miles:
  Before repeating required
Rarely used for shorter connections
  Due to cost

## Slide 64: MMF (Multimode Fiber)
Contains core with larger diameter than single-mode fiber
  Common sizes: 50 or 62.5 microns
Laser or LED generated light pulses travel at different angles
Greater attenuation than single-mode fiber
Common uses
  Cables connecting router to a switch
  Cables connecting server on network backbone

## Slide 65: Fiber-Optic Converters
Required to connect multimode fiber networks to single-mode fiber networks
  Also fiber- and copper-based parts of a network
Figure 3-38 Single-mode to multimode converter
Courtesy Omnitron Systems Technology

## Slide 66: Serial Cables
Data transmission style
  Pulses issued sequentially, not simultaneously
Serial transmission method
  RS-232
    Uses DB-9, DB-25, and RJ-45 connectors

## Slide 67: Structured Cabling
Cable plant
  Hardware that makes up the enterprise cabling system
Cabling standard
  TIA/EIA’s joint 568 Commercial Building Wiring Standard
    Also known as structured cabling
    Based on hierarchical design

## Slide 68
Figure 3-42 TIA/EIA structured cabling in an enterprise
Courtesy Course Technology/Cengage Learning

## Slide 69: Structured Cabling (cont’d.)
Components
  Entrance facilities
  MDF (main distribution frame)
  Cross-connect facilities
  IDF (intermediate distribution frame)
  Backbone wiring
  Telecommunications closet
  Horizontal wiring
  Work area

## Slide 70: Structured Cabling (cont’d.)
Table 3-2 TIA/EIA specifications for backbone cabling
Courtesy Course Technology/Cengage Learning

## Slide 71: Best Practices for Cable Installation and Management
Choosing correct cabling
  Follow manufacturers’ installation guidelines
  Follow TIA/EIA standards
Network problems
  Often traced to poor cable installation techniques
Installation tips to prevent Physical layer failures
  See Pages 121-122 in the text

## Slide 72: Summary
Information transmission methods
  Analog
  Digital
Multiplexing allows multiple signals to travel simultaneously over one medium
Full and half-duplex specifies whether signals can travel in both directions or one direction at a time
Noise distorts both analog and digital signals
Attenuation
  Loss of signal as it travels

## Slide 73: Summary (cont’d.)
Coaxial cable composed of core, insulator, shielding, sheath
Types of twisted pair cable
  Shielded and unshielded
Fiber-optic cable transmits data through light passing through the central fibers

## Slide 74: Summary (cont’d.)
Fiber-optic cable categories
  Single and multimode fiber
Serial communication often used for short connections between devices
Structured cabling standard provides wiring guidelines