## Slide 1: Network+ Guide to Networks 6th Edition
Chapter 5
Topologies and Ethernet Standards

## Slide 2: Objectives
Describe the basic and hybrid LAN topologies, and their uses, advantages, and disadvantages
Describe the backbone structures that form the foundation for most networks
Compare the different types of switching used in data transmission
Explain how nodes on Ethernet networks share a communications channel
Identify the characteristics of several Ethernet standards

## Slide 3: Simple Physical Topologies
Physical topology
  Physical network nodes layout
  Depicts broad scope
  Does not specify:
    Device types
    Connectivity methods
    Addressing schemes
Fundamental shapes
  Bus, ring, star
  Hybrid

## Slide 4: Bus
Bus topology
  Single cable
  Connects all network nodes
  No intervening connectivity devices
  One shared communication channel
Physical medium
  Coaxial cable
Passive topology
  Node listens for, accepts data
  Uses broadcast to send

## Slide 5: Bus (cont’d.)
Terminators
  50-ohm resistors
  Stop signal at end of wire
Signal bounce
  Signal travels endlessly between two network ends
One end grounded
  Removes static electricity

## Slide 6
Figure 5-1 A terminated bus topology network
Courtesy Course Technology/Cengage Learning

## Slide 7: Bus (cont’d.)
Bus topology advantage
  Relatively inexpensive
Disadvantages
  Does not scale well
  Difficult to troubleshoot
  Not very fault tolerant

## Slide 8: Ring
Ring topology
  Node connects to nearest two nodes
  Circular network
  Clockwise data transmission
    One direction (unidirectional) around ring
  Active topology
    Workstation participates in data delivery
    Data stops at destination
  Physical medium
    Twisted pair or fiber-optic cabling

## Slide 9: Ring (cont’d.)
Drawbacks
  Malfunctioning workstation can disable network
  Not very flexible or scalable
Figure 5-2 A ring topology network
Courtesy Course Technology/Cengage Learning

## Slide 10: Star
Star topology
  Node connects through central device
    Router or switch
Physical medium
  Twisted pair or fiber-optic cabling
Single cable connects only two devices
Advantage
  Fault tolerant
  Flexible

## Slide 11: Star (cont’d.)
Most popular fundamental layout
  Modern Ethernet networks based on star topology
1024 addressable logical network nodes maximum
Figure 5-3 A star topology network
Courtesy Course Technology/Cengage Learning

## Slide 12: Hybrid Topologies
Pure bus, ring, star topologies
  Rarely exist because too restrictive
Hybrid topology
  More likely
  Complex combination of pure topologies
  Several options

## Slide 13: Star-Wired Ring
Star-wired ring topology
  Star physical topology
  Ring logical topology
Benefit
  Star fault tolerance
Network use
  Token Ring networks
    IEEE 802.5

## Slide 14: Star-Wired Ring (cont’d.)
Figure 5-4 A star-wired ring topology network
Courtesy Course Technology/Cengage Learning

## Slide 15: Star-Wired Bus
Star-wired bus topology
  Workstation groups
    Star-connected devices
    Networked via single bus
Advantage
  Cover longer distances
  Easily interconnect, isolate different segments
Drawback
  Cabling, connectivity device expense
Basis for modern Ethernet networks

## Slide 16: Star-Wired Bus (cont’d.)
Figure 5-5 A star-wired bus topology network
Courtesy Course Technology/Cengage Learning

## Slide 17: Logical Topologies
Refers to way data transmitted between nodes
  Rather than physical layout
Does not necessarily match physical topology
Most common: bus and ring
Broadcast domain
  All nodes connected to single repeating device or switch

## Slide 18: Backbone Networks
Cabling connecting hubs, switches, routers
More throughput
Large organizations
  Fiber-optic backbone
  Cat 5 or better for hubs, switches
Enterprise-wide network backbones
  Complex, difficult to plan
Enterprise
  Entire organization
  Significant building block: backbone

## Slide 19: Serial Backbone
Simplest backbone
  Two or more devices
  Connect using single medium in daisy-chain fashion
Daisy-chain
  Linked series of devices
Benefit
  Logical growth solution
    Modular additions
  Low-cost LAN infrastructure expansion
    Easily attach switches

## Slide 20: Serial Backbone (cont’d.)
Backbone components
  Gateways, routers, switches
Figure 5-6 A serial backbone
Courtesy Course Technology/Cengage Learning

## Slide 21: Serial Backbone (cont’d.)
Serial connection of repeating devices
  Limited distance spanned between each
Standards
  Define number of repeating devices allowed
  Exceed standards
    Intermittent, unpredictable data transmission errors
Not used in modern networks

## Slide 22: Distributed Backbone
Connectivity devices
  Connected to hierarchy of central connectivity devices
Benefit
  Simple expansion, limited capital outlay
More complicated distributed backbone
  Connects multiple LANs, LAN segments using routers

## Slide 23: Distributed Backbone (cont’d.)
Additional benefits
  Workgroup segregation
  May include daisy-chain linked repeating devices
    Consider length
Drawback
  Potential for single failure points

## Slide 24
Figure 5-7 A simple distributed backbone
Courtesy Course Technology/Cengage Learning

## Slide 25
Figure 5-8 A distributed backbone connecting multiple LANs
Courtesy Course Technology/Cengage Learning

## Slide 26: Collapsed Backbone
Uses router or switch
  Single central connection point for multiple subnetworks
Highest layer
  Single router or switch with multiprocessors
Central router failure risk
Routers may slow data transmission
Advantages
  Interconnect different subnetwork types
  Central management

## Slide 27
Figure 5-9 A collapsed backbone
Courtesy Course Technology/Cengage Learning

## Slide 28: Parallel Backbone
Most robust network backbone
More than one central router, switch
  Connects to each network segment
Requires duplicate connections between connectivity devices
Advantage
  Redundant links
  Increased performance
  Better fault tolerance

## Slide 29
Figure 5-10 A parallel backbone
Courtesy Course Technology/Cengage Learning

## Slide 30: Switching
Logical network topology component
Determines connection creation between nodes
Three methods
  Circuit switching
  Packet switching
  Multiprotocol label switching

## Slide 31: Circuit Switching
Connection established between two network nodes
  Before transmitting data
Dedicated bandwidth
Data follows same initial path selected by switch
Monopolizes bandwidth while connected
  Resource wasted
Uses
  Live audio, videoconferencing
  Traditional telephone calls

## Slide 32: Packet Switching
Most popular
Breaks data into packets before transporting
Packets
  Travel any network path to destination
  Find fastest circuit available at any instant
  Need not follow each other
  Need not arrive in sequence
  Reassembled at destination
Requires speedy connections for live audio, video transmission

## Slide 33: MPLS (Multiprotocol Label Switching)
Introduced by IETF in 1999
Enables multiple types of Layer 3 protocols:
  To travel over any one of several Layer 2 protocols
Most often supports IP
Common use
  Layer 2 WAN protocols
Offers potentially faster transmission than packet- or circuit-switched networks

## Slide 34: MPLS (cont’d.)
Advantages
  Use packet-switched technologies over traditionally circuit switched networks
  Create end-to-end paths
  Addresses traditional packet switching limitations
  Better QoS (quality of service)
Figure 5-11 MPLS shim within a frame
Courtesy Course Technology/Cengage Learning

## Slide 35: Ethernet
Most popular networking technology used on modern LANs
Benefits
  Flexible
  Can run on various network media
  Excellent throughput
  Reasonable cost
All variations
  Share common access method
    CSMA/CD

## Slide 36: CSMA/CD (Carrier Sense Multiple Access with Collision Detection)
Network access method
  Controls how nodes access communications channel
  Necessary to share finite bandwidth
Carrier sense
  Ethernet NICs listen, wait until free channel detected
Multiple access
  Ethernet nodes simultaneously monitor traffic, access media

## Slide 37: CSMA/CD (cont’d.)
Collision
  Two nodes simultaneously:
    Check channel, determine it is free, begin transmission
Collision detection
  Manner nodes respond to collision
  Requires collision detection routine
    Enacted if node detects collision
  Jamming
    NIC issues 32-bit sequence
    Indicates previous message faulty

## Slide 38: CSMA/CD (cont’d.)
Heavily trafficked network segments
  Collisions common
Segment growth
  Performance suffers
  “Critical mass” number dependencies
    Data type and volume regularly transmitted
Collisions corrupt data, truncate data frames
  Network must detect and compensate

## Slide 39
Figure 5-12 CSMA/CD process
Courtesy Course Technology/Cengage Learning

## Slide 40: CSMA/CD (cont’d.)
Collision domain
  Portion of network where collisions occur
Ethernet network design
  Repeaters repeat collisions
    Result in larger collision domain
  Switches and routers
    Separate collision domains
Collision domains differ from broadcast domains

## Slide 41
Figure 5-13 Broadcast domains and collision domains
Courtesy Course Technology/Cengage Learning

## Slide 42: CSMA/CD (cont’d.)
Ethernet cabling distance limitations
  Effected by collision domains
Data propagation delay
  Data travel time too long
    Cannot identify collisions accurately
100 or 1000 Mbps networks
  Three segment maximum connected with two repeating devices
10 Mbps buses
  Five segment maximum connected with four repeating devices

## Slide 43: Ethernet Standards for Copper Cable
IEEE Physical layer standards
  Specify how signals transmit to media
  Differ significantly in signal encoding
    Affect maximum throughput, segment length, wiring requirements

## Slide 44: Ethernet Standards for Copper Cable (cont’d.)
10Base-T
  10 represents maximum throughput: 10 Mbps
  Base indicates baseband transmission
  T stands for twisted pair
  Two pairs of wires: transmit and receive
    Full-duplex transmission
  Follows 5-4-3 rule of networking
    Five network segments
    Four repeating devices
    Three populated segments maximum

## Slide 45
Figure 5-14 A 10Base-T network
Courtesy Course Technology/Cengage Learning

## Slide 46: Ethernet Standards for Copper Cable (cont’d.)
100Base-T (Fast Ethernet)
  IEEE 802.3u standard
  Similarities with 10Base-T
    Baseband transmission, star topology, RJ-45 connectors
  Supports three network segments maximum
    Connected with two repeating devices
    100 meter segment length limit between nodes
  100Base-TX
    100-Mbps throughput over twisted pair
    Full-duplex transmission: doubles effective bandwidth

## Slide 47
Figure 5-15 A 10Base-T network
Courtesy Course Technology/Cengage Learning

## Slide 48: Ethernet Standards for Copper Cable (cont’d.)
1000Base-T (Gigabit Ethernet)
  IEEE 802.3ab standard
  1000 represents 1000 Mbps
  Base indicates baseband transmission
  T indicates twisted pair wiring
  Four pairs of wires in Cat 5 or higher cable
    Transmit and receive signals
  Data encoding scheme: different from 100Base-T
  Standards can be combined
  Maximum segment length: 100 meters, one repeater

## Slide 49: Ethernet Standards for Copper Cable (cont’d.)
10GBase-T
  IEEE 802.3an
  Pushing limits of twisted pair
    Requires Cat 6, 6a, or 7 cabling
    Maximum segment length: 100 meters
  Benefits
    Very fast data transmission
    Cheaper than fiber-optic
  Uses
    Connect network devices
    Connect servers, workstations to LAN

## Slide 50: Ethernet Standards for Fiber-Optic Cable
100Base-FX (Fast Ethernet)
  100-Mbps throughput, baseband, fiber-optic cabling
    Multimode fiber containing at least two strands
  Half-duplex mode
    One strand receives; one strand transmits
    412 meters segment length
  Full duplex-mode
    Both strands send and receive
    2000 meters segment length
  One repeater maximum
  IEEE 802.3u standard

## Slide 51: Ethernet Standards for Fiber-Optic Cable (cont’d.)
1000Base-LX (1-Gigabit Ethernet)
  IEEE 802.3z standard
  1000: 1000-Mbps throughput
  Base: baseband transmission
  LX: reliance on 1300 nanometers wavelengths
  Longer reach than any other 1-gigabit technology
  Single-mode fiber: 5000 meters maximum segment
  Multimode fiber: 550 meters maximum segment
  One repeater between segments
  Excellent choice for long backbones

## Slide 52: Ethernet Standards for Fiber-Optic Cable (cont’d.)
1000Base-SX (1-Gigabit Ethernet)
  Differences from 1000Base-LX
    Multimode fiber-optic cable (installation less expensive)
    Uses short wavelengths (850 nanometers)
  Maximum segment length dependencies
    Fiber diameter, modal bandwidth used to transmit signals

## Slide 53: Ethernet Standards for Fiber-Optic Cable (cont’d.)
1000Base-SX (cont’d.)
  Modal bandwidth measurement
    Highest frequency of multimode fiber signal (over specific distance)
    MHz-km
    Higher modal bandwidth, multimode fiber caries signal reliably longer
  50 micron fibers: 550 meter maximum length
  62.5 micron fibers: 275 meter maximum length
  One repeater between segments
  Best suited for shorter network runs

## Slide 54: 10-Gigabit Fiber-Optic Standards
Extraordinary potential for fiber-optic cable
  Pushing limits
802.3ae standard
  Fiber-optic Ethernet networks
  Transmitting data at 10 Gbps
  Several variations
  Common characteristics
    Star topology, allow one repeater, full-duplex mode
  Differences
    Signal’s light wavelength; maximum allowable segment length

## Slide 55: 10-Gigabit Fiber-Optic Standards (cont’d.)
10GBase-SR and 10GBase-SW
  10G: 10 Gbps
  Base: baseband transmission
  S: short reach
  Physical layer encoding
    R works with LAN fiber connections
    W works with SONET fiber connections
  Multimode fiber: 850 nanometer signal transmission
  Maximum segment length
    Depends on fiber diameter

## Slide 56: 10-Gigabit Fiber-Optic Standards (cont’d.)
10GBase-LR and 10GBase-LW
  10G: 10 Gbps
  Base: baseband transmission
  L: long reach
  Single-mode fiber: 1310 nanometer signal transmission
  Maximum segment length
    10,000 meters
  10GBase-LR: WAN or MAN
  10GBase-LW: SONET WAN links

## Slide 57: 10-Gigabit Fiber-Optic Standards (cont’d.)
10GBase-ER and 10GBase-EW
  E: extended reach
  Single-mode fiber
    Transmit signals with 1550 nanometer wavelengths
  Longest fiber-optic segment reach
    40,000 meters (25 miles)
  10GBase-EW
    Encoding for SONET
  Best suited for WAN use

## Slide 58: Summary of Common Ethernet Standards
Table 5-1 Common Ethernet standards
Courtesy Course Technology/Cengage Learning

## Slide 59
Courtesy Course Technology/Cengage Learning
Figure 5-16 Multiple types of Ethernet on a WAN

## Slide 60: Ethernet Frames
Four types
  Ethernet_802.2 (Raw)
  Ethernet_802.3 (Novell proprietary)
  Ethernet_II (DIX)
  Ethernet_SNAP
Frame types differ slightly
  Coding and decoding packets
No relation to topology, cabling characteristics
Framing
  Independent of higher-level layers

## Slide 61: Using and Configuring Frames
Ensure all devices use same, correct frame type
  Node communication
Ethernet_II used today
Frame type configuration
  Specified using NIC configuration software
  NIC autodetect
Importance
  Know frame type for troubleshooting

## Slide 62: Frame Fields
Common fields
  7-byte preamble, 1-byte start-of-frame delimiter
  SFD (start-of-frame delimiter) identifies where data field begins
  14-byte header
  4-byte FCS (frame check sequence)
  Frame size range: 64 to 1518 total bytes
Larger frame sizes result in faster throughput
Improve network performance
  Properly manage frames

## Slide 63: Ethernet_II (DIX)
Developed by DEC, Intel, Xerox (abbreviated DIX)
  Before IEEE
Contains 2-byte type field
  Identifies the Network layer protocol
Most commonly used on contemporary Ethernet networks
Figure 5-17 Ethernet II (DIX) frame
Courtesy Course Technology/Cengage Learning

## Slide 64: PoE (Power over Ethernet)
IEEE 802.3af standard
  Supplying electrical power over Ethernet connections
Two device types
  PSE (power sourcing equipment)
  PDs (powered devices)
Requires Cat 5 or better copper cable
Connectivity devices must support PoE
Compatible with current 802.3 installations

## Slide 65: PoE (cont’d.)
Figure 5-18 PoE capable switch
Figure 5-19 PoE adapters
Courtesy D-Link North America
Courtesy D-Link North America

## Slide 66: Summary
Physical topology describes basic network physical layout
  Examples: bus, ring, star, hybrid
Logical topology describes signal transmission
Network backbones
  Serial, distributed, collapsed, parallel
Switching
  Manages packet filtering, forwarding
Ethernet
  Cabling specifications, data frames, PoE