## Slide 1: Network+ Guide to Networks 6th Edition
Chapter 6
Network Hardware, Switching, and Routing

## Slide 2: Objectives
Identify the functions of LAN connectivity hardware
Install, configure, and differentiate between network devices such as NICs, hubs, bridges, switches, routers, and gateways
Explain the advanced features of a switch and understand popular switching techniques, including VLAN management
Explain the purposes and properties of routing
Describe common IPv4 and IPv6 routing protocols

## Slide 3: NICs (Network Interface Cards)
Connectivity devices
  Enable device transmission
  Transceiver
    Transmits and receives data
Physical layer and Data Link layer functions
  Issue data signals
  Assemble and disassemble data frames
  Interpret physical addressing information
  Determine right to transmit data

## Slide 4: NICs (cont’d.)
Smart hardware
  Prioritization
  Network management
  Buffering
  Traffic-filtering
Do not analyze information
  Added by Layers 3 through 7 OSI model protocols
Importance
  Common to every networking device, network

## Slide 5: Types of NICs
Before ordering or installing NIC
  Know device interface type
NIC dependencies
  Access method
  Network transmission speed
  Connector interfaces
  Compatible motherboard or device type
  Manufacturer
  Support for enhanced features

## Slide 6: Types of NICs (cont’d.)
Bus
  Circuit, signaling pathway
  Motherboard uses to transmit data to computer’s components
    Memory, processor, hard disk, NIC
  Differ according to capacity
    Defined by data path width and clock speed
  Data path size
    Parallel bits transmitting at any given time
    Proportional to attached device’s speed

## Slide 7: Types of NICs (cont’d.)
Expansion slots
  Multiple electrical contacts on motherboard
  Allow bus expansion
Expansion card (expansion board)
  Circuit board for additional devices
  Inserts into expansion slot, establishes electrical connection
  Device connects to computer’s main circuit or bus
  Computer centrally controls device

## Slide 8: Types of NICs (cont’d.)
Multiple bus types
  PCIe bus: most popular expansion board NIC
PCIe (Peripheral Component Interconnect Express)
  32-bit bus
  Maximum data transfer rate: 1 Gbps
  Introduced in 2004
Figure 6-1 PCIe expansion board NIC
Courtesy of Intel Corporation

## Slide 9: Types of NICs (cont’d.)
Determining bus type
  Read documentation
  Look inside PC case
  If more than one expansion slot type:
    Refer to NIC, PC manufacturers’ guidelines
    Choose NIC matching most modern bus

## Slide 10: Types of NICs (cont’d.)
Peripheral NICs
  Attached externally
  Simple installation into a variety of slots
    PCMCIA
    USB
    CompactFlash
    FireWire
  Installing and configuring software may be required

## Slide 11: Types of NICs (cont’d.)
Figure 6-2 A USB NIC
© Charles B. Ming Onn/Shutterstock.com

## Slide 12: Types of NICs (cont’d.)
On-Board NICs
  Connect device directly to motherboard
  On-board ports: mouse, keyboard
New computers, laptops
  Use onboard NICs integrated into motherboard
Advantages
  Saves space
  Frees expansion slots

## Slide 13: Types of NICs (cont’d.)
Figure 6-3 Motherboard with on-board NICs
Courtesy of EVGA USA

## Slide 14: Installing and Configuring NICs
Installing NIC hardware
  Read manufacturer’s documentation
Install expansion card NIC
  Gather needed tools
  Unplug computer, peripherals, and network cable
  Ground yourself
  Open computer case
    Select slot, insert NIC, attach bracket, verify cables
  Replace cover, turn on computer
    Configure NIC software

## Slide 15: Installing and Configuring NICs (cont’d.)
Figure 6-4 A properly inserted expansion board NIC
Courtesy of Gary Herrington Photography

## Slide 16: Installing and Configuring NICs (cont’d.)
Installing and configuring NIC software
  Device driver
    Software enabling device to communicate with operating system
Purchased computer with a peripheral
  Drivers installed
Add hardware to computer
  Must install drivers

## Slide 17: Installing and Configuring NICs (cont’d.)
Operating system built-in drivers
  Automatically recognize hardware, install drivers
Drivers not available from operating system
  Install and configure NIC software
  Available at manufacturer’s Web site

## Slide 18: Installing and Configuring NICs (cont’d.)
Verifying NIC functionality
  Check whether device can communicate with network
Diagnostic tools
  Use manufacturer’s configuration utility
    Loopback plug needed
  Visual inspection of LEDs
    Read manufacturer’s documentation
  Use simple commands
    Example: pinging the loopback address

## Slide 19: Modular Interfaces
Hot-swappable components
  Can be changed without disrupting operations
GBIC (Gigabit interface converter)
  Standard type of modular interface
  May contain RJ-45 or fiber-optic cable ports
SFPs (small form-factor pluggable)
  Provide same form factor as GBIC
    Allow more ports per inch

## Slide 20: Modular Interfaces (cont’d.)
Figure 6-8 SFP (small form-factor pluggable) transceiver for use with fiber connections
Figure 6-7 GBIC (Gigabit interface converter) with an RJ-45 port
Courtesy Course Technology/Cengage Learning
Courtesy Course Technology/Cengage Learning

## Slide 21: Repeaters and Hubs
Repeaters
  Operate in Physical OSI model layer
  No means to interpret data
  Regenerate signal
Hub
  Repeater with more than one output port
  Typically contains multiple data ports
    Patch cables connect printers, servers, and workstations
  Most contain uplink port

## Slide 22: Bridges
Devices that connect two network segments
Analyze incoming frames
  Make decisions on where to direct them
Operate at Data Link OSI model layer
Single input and single output ports
Protocol independent
Filtering database
  Contains known MAC addresses and network locations

## Slide 23: Bridges (cont’d.)
Figure 6-10 A bridge’s use of a filtering database
Courtesy Course Technology/Cengage Learning

## Slide 24: Switches
Connectivity devices that subdivide a network
  Segments
Traditional switches
  Operate at Data Link OSI model layer
Modern switches
  Can operate at Layer 3 or Layer 4
Switches interpret MAC address information
Common switch components
  Internal processor, operating system, memory, ports

## Slide 25: Switch Installation
Follow manufacturer’s guidelines
General steps (assume Cat 5 or better UTP)
  Verify switch placement
  Turn on switch
  Verify lights, self power tests
  Configure (if necessary)
  Connect NIC to a switch port (repeat for all nodes)
  After all nodes connected, turn on nodes
  Connect switch to larger network (optional)

## Slide 26: Switch Installation (cont’d.)
Figure 6-13 A switch on a small network
Courtesy Course Technology/Cengage Learning

## Slide 27: Switching Methods
Difference in switches
  Incoming frames interpretation
  Frame forwarding decisions making
Four switching modes exist
  Two basic methods discussed
    Cut-through mode
    Store-and-forward mode

## Slide 28: Switching Methods (cont’d.)
Cut-through mode
  Switch reads frame’s header
  Forwarding decision made before receiving entire packet
    Uses frame header: first 14 bytes contains destination MAC address
  Cannot verify data integrity using frame check sequence
  Can detect erroneously shortened packets (runts)
  Runt detected: wait for integrity check

## Slide 29: Switching Methods (cont’d.)
Cut-through mode (cont’d.)
  Cannot detect corrupt packets
  Advantage: speed
  Disadvantage
    Data buffering (switch flooded with traffic)
  Best use
    Small workgroups needing speed
    Low number of devices

## Slide 30: Switching Methods (cont’d.)
Store-and-forward mode
  Switch reads entire data frame into memory
  Checks for accuracy before transmitting information
  Transmit data more accurately than cut-through mode
  Slower than cut-through mode
  Best uses
    Larger LAN environments; mixed environments
  Can transfer data between segments running different transmission speeds

## Slide 31: VLANs and Trunking
VLANs (virtual local area networks)
  Logically separate networks within networks
    Groups ports into broadcast domain
Broadcast domain
  Port combination making a Layer 2 segment
  Ports rely on Layer 2 device to forward broadcast frames
Collision domain
  Ports in same broadcast domain
    Do not share single channel

## Slide 32
Figure 6-14 A simple VLAN design
Courtesy Course Technology/Cengage Learning

## Slide 33: VLANs and Trunking (cont’d.)
Advantage of VLANs
  Flexible
    Ports from multiple switches or segments
    Use any end node type
  Reasons for using VLAN
    Separating user groups
    Isolating connections
    Identifying priority device groups
    Grouping legacy protocol devices
    Separating large network into smaller subnets

## Slide 34: VLANs and Trunking (cont’d.)
Switch typically preconfigured
  One default VLAN
  Cannot be deleted or renamed
Create additional VLANs
  Indicate to which VLAN each port belongs
  Additional specifications
    Security parameters, filtering instructions, port performance requirements, network addressing and management options
Maintain VLAN using switch software

## Slide 35: VLANs and Trunking (cont’d.)
Potential problem
  Cutting off group from rest of network
    Correct by using router or Layer 3 switch
Trunking
  Switch’s interface carries traffic of multiple VLANs
Trunk
  Single physical connection between switches
VLAN data separation
  Frame contains VLAN identifier in header

## Slide 36: VLANs and Trunking (cont’d.)
Figure 6-16 Trunk for multiple VLANs
Courtesy Course Technology/Cengage Learning

## Slide 37: STP (Spanning Tree Protocol)
IEEE standard 802.1D
Operates in Data Link layer
Prevents traffic loops
  Calculating paths avoiding potential loops
  Artificially blocking links completing loop
Three steps
  Select root bridge based on Bridge ID
  Examine possible paths between network bridge and root bridge
  Disables links not part of shortest path

## Slide 38
Figure 6-17 Enterprise-wide switched network
Courtesy Course Technology/Cengage Learning

## Slide 39
Figure 6-18 STP-selected paths on a switched network
Courtesy Course Technology/Cengage Learning

## Slide 40: STP (cont’d.)
History
  Introduced in 1980s
    Original STP too slow
  RSTP (Rapid Spanning Tree Protocol)
    Newer version
    IEEE’s 802.1w standard
Cisco and Extreme Networks
  Proprietary versions
No enabling or configuration needed
  Included in switch operating software

## Slide 41: Content and Multilayer Switches
Layer 3 switch (routing switch)
  Interprets Layer 3 data
Layer 4 switch
  Interprets Layer 4 data
Content switch (application switch)
  Interprets Layer 4 through Layer 7 data
Advantages
  Advanced filtering
  Keeping statistics
  Security functions

## Slide 42: Content and Multilayer Switches (cont’d.)
Distinguishing between Layer 3 and Layer 4 switch
  Manufacturer dependent
Higher-layer switches
  Cost more than Layer 2 switches
  Used in network backbone

## Slide 43: Routers
Multiport connectivity device
  Directs data between network nodes
  Integrates LANs and WANs
    Different transmission speeds, protocols
Operate at Network layer (Layer 3)
  Directs data from one segment or network to another
  Logical addressing
  Protocol dependent
Slower than switches and bridges
  Need to interpret Layers 3 and higher information

## Slide 44: Routers (cont’d.)
Traditional stand-alone LAN routers
  Being replaced by Layer 3 routing switches
New niche
  Specialized applications
    Linking large Internet nodes
    Completing digitized telephone calls

## Slide 45: Router Characteristics and Functions
Intelligence
  Tracks node location
  Determine shortest, fastest path between two nodes
  Connects dissimilar network types
Large LANs and WANs
  Routers indispensable
Router components
  Internal processor, operating system, memory, input and output jacks, management control interface

## Slide 46: Router Characteristics and Functions (cont’d.)
Multiprotocol routers
  Multiple slots
  Accommodate multiple network interfaces
Inexpensive routers
  Home, small office use

## Slide 47
Figure 6-19 Routers
Courtesy Course Technology/Cengage Learning

## Slide 48: Router Characteristics and Functions (cont’d.)
Router capabilities
  Connect dissimilar networks
  Interpret Layer 3 addressing
  Determine best data path
  Reroute traffic

## Slide 49: Router Characteristics and Functions (cont’d.)
Optional router functions
  Filter broadcast transmissions
  Enable custom segregation, security
  Support simultaneous connectivity
  Provide fault tolerance
  Monitor network traffic
  Diagnose problems and trigger alarms

## Slide 50: Router Characteristics and Functions (cont’d.)
Interior router
  Directs data between nodes on a LAN
Exterior router
  Directs data between nodes external to a LAN
Border routers
  Connect autonomous LAN with a WAN
Routing tables
  Identify which routers serve which hosts

## Slide 51: Router Characteristics and Functions (cont’d.)
Static routing
  Router configured to use specific path between nodes
Dynamic routing
  Automatically calculates best path between nodes
Installation
  Simple for small office or home office LANs
    Web-based configuration
  Challenging for sizable networks

## Slide 52
Figure 6-20 The placement of routers on a LAN
Courtesy Course Technology/Cengage Learning

## Slide 53: Routing Protocols
Best path
  Most efficient route from one node to another
  Dependent on:
    Hops between nodes
    Current network activity
    Unavailable link
    Network transmission speed
    Topology
  Determined by routing protocol

## Slide 54: Routing Protocols (cont’d.)
Routing metric factors
  Number of hops
  Throughput on potential path
  Delay on a potential path
  Load (traffic)
  Maximum transmission unit (MTU)
  Cost
  Reliability of potential path

## Slide 55: Routing Protocols (cont’d.)
Router convergence time
  Time router takes to recognize best path
    Change or network outage event
  Distinguishing feature
    Overhead; burden on network to support routing protocol

## Slide 56: Routing Protocols (cont’d.)
Distance-vector routing protocols
  Determine best route based on distance to destination
  Factors
    Hops, latency, network traffic conditions
RIP (Routing Information Protocol)
  Only factors in number of hops between nodes
    Limits 15 hops
  Type of IGP (Interior Gateway Protocol)
    Can only route within internal network
  Slower and less secure than other routing protocols

## Slide 57: Routing Protocols (cont’d.)
RIPv2 (Routing Information Protocol Version 2)
  Generates less broadcast traffic, more secure
  Cannot exceed 15 hops
  Less commonly used
BGP (Border Gateway Protocol)
  Communicates using BGP-specific messages
  Many factors determine best paths
  Configurable to follow policies
  Type of EGP (Exterior Gateway Protocol)
  Most complex (choice for Internet traffic)

## Slide 58: Routing Protocols (cont’d.)
Link-state routing protocol
  Routers share information
    Each router independently maps network, determines best path
OSPF (Open Shortest Path First)
  Interior or border router use
  No hop limit
  Complex algorithm for determining best paths
  Each OSPF router
    Maintains database containing other routers’ links

## Slide 59: Routing Protocols (cont’d.)
IS-IS (Intermediate System to Intermediate System)
  Codified by ISO
  Interior routers only
  Supports two Layer 3 protocols
    IP
    ISO-specific protocol
  Less common than OSPF

## Slide 60: Routing Protocols (cont’d.)
Hybrid
  Link-state and distance-vector characteristics
  EIGRP (Enhanced Interior Gateway Routing Protocol)
    Most popular
    Cisco network routers only
  EIGRP benefits
    Fast convergence time, low network overhead
    Easier to configure and less CPU-intensive than OSPF
    Supports multiple protocols
    Accommodates very large, heterogeneous networks

## Slide 61: Routing Protocols (cont’d.)
Table 6-1 Summary of common routing protocols
Courtesy Course Technology/Cengage Learning

## Slide 62: Gateways and Other Multifunction Devices
Gateway
  Combination of networking hardware and software
  Connects two systems using different formatting, communications protocols, architecture
  Repackages information
  Resides on servers, microcomputers, connectivity devices, mainframes
Popular gateways
  E-mail gateway, Internet gateway, LAN gateway, voice/data gateway, firewall

## Slide 63: Summary
Network adapter types vary
  Access method, transmission speed, connector interfaces, number of ports, manufacturer, device type
Repeaters
  Regenerate digital signal
Bridges can interpret the data they retransmit
Switches subdivide a network
  Generally secure
  Create VLANs
Various routing protocols exist